## Slide 1
Ring Amplifier for Scalable Amplification
Arkadeep Barua
[203079009]
Department of Electrical Engineering
Indian Institute of Technology, Bombay
Supervisor : Prof Rajesh Zele
M.Tech. Seminar

## Slide 2
Arkadeep Barua
Content
Motivation
Ring Amplifier Operation Theory and Stabilization
Ring Amplifier Advantages
Ring Amplifier Design Considerations
Ring Amplifier Topologies
Amplifier Performance Enhancement Technique: CLS

## Slide 3
Arkadeep Barua
Motivation
As we are moving towards lower technology node amplifier design is becoming challenging.
With reduction of supply voltage performance of conventional opamp is declining.
Conventional amplifiers not downscaled well.
Some ADC architectures like pipeline ADC facing scaling bottleneck due to Amplifier.
Ring Amplifier is scalable amplifier.
Ring Amplifier can perform efficiently in scaled environment.

## Slide 4
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.
Arkadeep Barua
Ring Oscillator Characteristics
Properties of Ring Oscillator
large gain.
rail to rail swing.
maximal slewing efficiency.
small, simple layout.
fully compatible with digital CMOS.
The main problem it is an oscillator.
Fig. Ring Oscillator into a switched feedback structure
Fig. Input output waveforms of Ring Oscillator

## Slide 5
[2] B. Hershberg, Un-Ku Moon, “The Ring Amplifier: Scalable Amplification With Ring Oscillators,” in book: High-Performance AD and DA Converters, July. 2015.
Arkadeep Barua
Ring Oscillator Stabilization
Pole Stabilization:
By placing one of the pole at lower frequency.
Stabilize with p3 or p1.
Placing p1 at lower frequency using miller compensation.
Placing p3 at lower frequency using progressive reduction of overdrive voltage.
Fig. Position of Poles for a Stable System

## Slide 6
Arkadeep Barua
Ring Amplifier Dynamic Behaviour
Initial charging phase poles will be placed much tighter.
Unstable but have high bandwidth.
At steady state one pole pushed down to lower frequency.
Fig. Dynamic behavior of Ring Amplifier
[2] B. Hershberg, Un-Ku Moon, “The Ring Amplifier: Scalable Amplification With Ring Oscillators,” in book: High-Performance AD and DA Converters, July. 2015.

## Slide 7
Arkadeep Barua
Ring Amplifier Fundamentals: Dynamic Large Signal Stabilization
Fig. Ring Amplifier placed into switched capacitor feedback
A ring amplifier is created by splitting a ring oscillator into two signal paths and embedding a different offset in each path.
When placed in switched-capacitor feedback, a set of internal mechanisms generate stability and allow the oscillator to be used as an amplifier.
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 8
Arkadeep Barua
Ring Amplifier Fundamentals: Dynamic Large Signal Stabilization Working
Fig. Input and output charging waveforms of Ring Amplifier when placed in the switched capacitor feedback structure
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 9
Arkadeep Barua
Fig. Three figures of Input and output charging waveforms of Ring Amplifier when placed in the switched capacitor feedback structure with dead zone voltage of 0mv, 300mV and 400mV
At Vdeadzone= 0mV it oscillates.
as we increase the offset voltage stability increases.
And finally biasing condition when ring amplifier become so stable that almost immediately locked into the steady state configuration.
Ring Amplifier Fundamentals: Effect of increasing Offset Voltage
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 10
Arkadeep Barua
Ring Amplifier Three Operation Phases: Slew Phase
Slew: One of the output stage transistor will drive with max overdrive current onto the load capacitance. The slew rate is given by:
Slew Phase
Fig. Input and output charging waveforms of Ring Amplifier when placed in the switched capacitor feedback structure
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 11
Arkadeep Barua
Ring Amplifier Three Operation Phases: Stabilization Phase
Stabilization: progressive reduction of overdrive voltage force the ring amplifier into a stable configuration.
Stabilization Phase
Steps of progressive reduction of overdrive voltage that stabilize the Ring Amplifier
Reduction of average overdrive voltage.
Reduction of output current.
Reduction of amplitude.
Fig. Input and output charging waveforms of Ring Amplifier when placed in the switched capacitor feedback structure
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 12
Arkadeep Barua
Ring Amplifier Three Operation Phases: Steady Phase
Steady Phase
Steady State:
 The output pole is pushed to stabilizing frequency.
 Low quiescent current on the output stage => Vdsat requirement very small => very large output swing without running into compression problems
Fig. Input and output charging waveforms of Ring Amplifier when placed in the switched capacitor feedback structure
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.

## Slide 13
[6] C. Y. Lee, P. K. Venkatachala, A. ElShater, B. Xiao, H. Hu and Un K. Moon, ”Cascoded Ring Ampli- fiers for High Speed and High Accuracy Settling,” 2019 IEEE International Symposium on Circuits and Systems (ISCAS), 2019.
Arkadeep Barua
Ring Amplifier AC Analysis
Gain: The small-signal gain of a single inverter is given by:
The load capacitor for stage 1 and 2 are defined as:
The right half plane zero in each stage is given as:
The small signal transfer function of the stage inverter is
given by:
Fig. Ring Amplifier

## Slide 14
Arkadeep Barua
Ring Amplifier AC Analysis
Gain: The overall small signal transfer function of the ring amplifier in steady state is given by:
. .
The feedback factor is
The loop transfer function ignoring high frequency poles and zeros is given as:
. .
[6] C. Y. Lee, P. K. Venkatachala, A. ElShater, B. Xiao, H. Hu and Un K. Moon, ”Cascoded Ring Ampli- fiers for High Speed and High Accuracy Settling,” 2019 IEEE International Symposium on Circuits and Systems (ISCAS), 2019.

## Slide 15
Arkadeep Barua
Ring Amplifier Advantages: Slew Based Charging
charge the output with slew-based ramping.
even for large capacitive loads, small transistor sizes can still produce high slew rates.
with small output transistors, the second stage inverters will be negligibly loaded.
This effectively decouples the internal power requirements from that of the output load size.
Fig. Ring Amplifier placed into switch capacitor feedback
[4] K. M. Megawer, F. A. Hussien, M. M. Aboudina and A. N. Mohieldin, ”A Systematic Design Methodology for Class-AB-Style Ring Amplifiers,” in IEEE Transactions on Circuits and Systems II: Express Briefs, Sept. 2018.

## Slide 16
Arkadeep Barua
Ring Amplifier Advantages: Performance with Scaling
Ring Amplifier must operate efficiently in a scaled environment.
power consumption is governed by inverter power-delay product.
ringamp’s inverter chain propagation delay, td scales as a function of minimum feature size, leading to improvement of speed, accuracy, and power.
static current reduces as we scale down.
Fig. Ring Amplifier placed into switch capacitor feedback
[4] K. M. Megawer, F. A. Hussien, M. M. Aboudina and A. N. Mohieldin, ”A Systematic Design Methodology for Class-AB-Style Ring Amplifiers,” in IEEE Transactions on Circuits and Systems II: Express Briefs, Sept. 2018.

## Slide 17
Arkadeep Barua
Ring Amplifier Noise Analysis
Noise:
Thermal noise dominates the noise performance. The thermal noise of an inverter is given
Higher transconductance leads to lower input-referred noise and as a result, the first stage is the most power hungry stage in a noise limited ring amplifier.
Fig. Ring Amplifier placed into switch capacitor feedback

## Slide 18
Arkadeep Barua
Ring Amplifier Speed Analysis
Speed: The settling time comprises of slewing time and stabilization time.
This time will depend on the BW settling of the ring amplifier.
The slew rate is given by:
Due to Tdelay (total loop delay), this phase ends with an overshoot voltage Vovershoot given by:
An optimum point needs to be reached between the slew rate of the third inverter and the delay of the first two inverters.
choose the (W/L) of the third stage and (W/L) of second stage to reach optimum point between slew rate and delay.
Fig. Transient output of Ring Amplifier placed into switch capacitor feedback
[4] K. M. Megawer, F. A. Hussien, M. M. Aboudina and A. N. Mohieldin, ”A Systematic Design Methodology for Class-AB-Style Ring Amplifiers,” in IEEE Transactions on Circuits and Systems II: Express Briefs, Sept. 2018.

## Slide 19
Arkadeep Barua
Ring Amplifier Design Methodology
Step 1: Choose L for suitable gain.
 Step 2: Choose the ratio between (W/L) of NMOS and PMOS to adjust the inverter’s trip-point to VCM (VDD/2 to increase the output voltage swing) or to match the gm of both transistors.
 Step 3: The width of the third inverter stage (W3) is set to meet the slew rate requirement derived from the settling time requirement.
 Step 4: The width of the first inverter stage (W1) is set to satisfy the noise requirement as an initial sizing for a noise limited design.
 Step 5: The width of the second inverter stage (W2) is set to determine the required delay for a minimum Vovershoot. This is derived from the settling time requirement.
An optimized design of a ring amplifier lies in resolving the mentioned trade-offs and reaching the values for circuit parameters to achieve the required specifications.
The hand-calculated circuit parameters may require some adjustments after being simulated.

## Slide 20
Arkadeep Barua
Ring Amplifier Topologies
Offset voltage applied directly before output.
Precise control of output stage biasing.
Best for Class AB operation.
Limitations: reduce max slewing efficiency.
Fig. Ring amplifier with biasing at the third stage
[4] K. M. Megawer, F. A. Hussien, M. M. Aboudina and A. N. Mohieldin, ”A Systematic Design Methodology for Class-AB-Style Ring Amplifiers,” in IEEE Transactions on Circuits and Systems II: Express Briefs, Sept. 2018.
Ring Amplifier with Biasing at Third Stage:

## Slide 21
Arkadeep Barua
Ring Amplifier Topologies
dropping of series voltage in line with gate of output transistor resolved.
Dynamically creates offset voltage across register during stabilization.
PVT robust design. If supply voltage increase => current through register also increase => offset voltage increases and keep Iout stable.
Slewing efficiency is more.
Limitations: Speed problem if large VDZ is needed.
Fig. Self Biased Ring Amplifier
[5] Y. Lim and M. P. Flynn, ”A 100 MS/s, 10.5 Bit, 2.46 mW Comparator Less Pipeline ADC Using Self- Biased Ring Amplifiers,” in IEEE Journal of Solid-State Circuits, Oct. 2015.
Self Biased Ring Amplifier:

## Slide 22
Arkadeep Barua
Ring Amplifier Topologies
Increasing the number of stages increase power consumption, large signal delay effecting stability.
Increasing the output impedance of the first two stages reduce associated pole frequency.
Increasing L of output transistor reduce slew rate.
Increasing W of output transistor reduce zero.
Output impedance can be increased using cascode device.
Fig. Cascode Ring Amplifier structure
[6] C. Y. Lee, P. K. Venkatachala, A. ElShater, B. Xiao, H. Hu and Un K. Moon, ”Cascoded Ring Ampli- fiers for High Speed and High Accuracy Settling,” 2019 IEEE International Symposium on Circuits and Systems (ISCAS), 2019.
Cascode Ring Amplifier:

## Slide 23
Arkadeep Barua
Ring Amplifier Topologies
Tunable ON state resistance.
Power cycling.
Limitations: Less PVT robust than static resistor.
Can control the propagation delay with this current starved inverter structure.
Control delay.
Analog PVT tracking scheme.
Limitations: Slower.
[3] Z. Pei, Y. Wang and L. Han, ”CMOS Ring Amplifier for Bio-Signal LNA,” 2020 IEEE 4th Information Technology, Networking, Electronic and Automation Control Conference (ITNEC), 2020.
Ring Amplifier Biasing with Transistor:

## Slide 24
Arkadeep Barua
Amplifier Performance Enhancement: CLS Structure
CLS(correlated level shift) technique:
reduce finite amplifier gain error
increase the amplifier’s useful output swing
amplification phase happens in two steps: estimation(EST) and level shifting(CLS) .
An estimate of the signal is generated during φEST and sampled onto CCLS, which is then placed in the feedback path in order to cancel finite opamp gain error during φCLS.
Fig. Basic CLS structure
[7] Gregoire, B. Robert. “Correlated level shifting as a power-saving method to reduce the effects of finite DC gain and signal swing in opamps.” (2008).

## Slide 25
Arkadeep Barua
CLS Structure Working Mechanism
In Estimation phase:
The residual voltage on C1 from the imperfect
virtual ground is
There is two ways to reduce residual voltage on C1
1. Increase gain of opamp AEST (conventional method)
2. Decrease (CLS method)
In Level Shift phase:
Now the residual voltage on C1 is
[7] Gregoire, B. Robert. “Correlated level shifting as a power-saving method to reduce the effects of finite DC gain and signal swing in opamps.” (2008).
Where,

## Slide 26
Arkadeep Barua
Amplifier Error Calculation in CLS Technique
26 / 31
= 
Assuming thatand

## Slide 27
Arkadeep Barua
CLS Structure Modification: Split CLS Structure
Fig. Basic Split CLS structure
Advantage of split CLS over CLS
Can use different amplifier at estimation and CLS phase as per requirement.
AMP1 requires large output swing and high slewing capabilities. So can use ring amplifier
AMP2 only processes the small error term left over from AMP1, and requires a much smaller output swing and slew rate. So can use cascode opamp.
[8] B. Hershberg, S. Weaver and U. Moon, ”Design of a Split-CLS Pipelined ADC With Full Signal Swing Using an Accurate But Fractional Signal Swing Opamp,” in IEEE Journal of Solid-State Circuits, Dec. 2010.

## Slide 28
Arkadeep Barua
Conclusion
Ring amplifier has promising performance in a scaled environment.
Ring amplifier is compatible with techniques like CLS, which counter finite amplifier gain problems.
Due to the unique properties of ring amplifiers, their use can be explored in many other amplifier-dependent analog blocks.

## Slide 29
Arkadeep Barua
References
[1] B. Hershberg, S. Weaver, K. Sobue, S. Takeuchi, K. Hamashita and U. Moon, ”Ring Amplifiers for Switched Capacitor Circuits,” in IEEE Journal of Solid-State Circuits, Dec. 2012.
[2] B. Hershberg, Un-Ku Moon, “The Ring Amplifier: Scalable Amplification With Ring Oscillators,” in book: High-Performance AD and DA Converters, July. 2015.
[3] Z. Pei, Y. Wang and L. Han, ”CMOS Ring Amplifier for Bio-Signal LNA,” 2020 IEEE 4th Information Technology, Networking, Electronic and Automation Control Conference (ITNEC), 2020.
[4] K. M. Megawer, F. A. Hussien, M. M. Aboudina and A. N. Mohieldin, ”A Systematic Design Methodology for Class-AB-Style Ring Amplifiers,” in IEEE Transactions on Circuits and Systems II: Express Briefs, Sept. 2018.
[5] Y. Lim and M. P. Flynn, ”A 100 MS/s, 10.5 Bit, 2.46 mW Comparator Less Pipeline ADC Using Self- Biased Ring Amplifiers,” in IEEE Journal of Solid-State Circuits, Oct. 2015.
[6] C. Y. Lee, P. K. Venkatachala, A. ElShater, B. Xiao, H. Hu and Un K. Moon, ”Cascoded Ring Ampli- fiers for High Speed and High Accuracy Settling,” 2019 IEEE International Symposium on Circuits and Systems (ISCAS), 2019.
[7] Gregoire, B. Robert. “Correlated level shifting as a power-saving method to reduce the effects of finite DC gain and signal swing in opamps.” (2008).
[8] B. Hershberg, S. Weaver and U. Moon, ”Design of a Split-CLS Pipelined ADC With Full Signal Swing Using an Accurate But Fractional Signal Swing Opamp,” in IEEE Journal of Solid-State Circuits, Dec. 2010.

## Slide 30
Arkadeep Barua
Thank You